## Slide 1
For a 1x2x1 SC-BCC Column
Presented By: Alec Perkins
working under Dr. Patrick Ziemke
With ABAQUS and Python Graphing
Force-Displacement Curve

## Slide 2
01
02
03
Units and Material
Parts and Assembly
Boundary Conditions
Contents
04
05
06
Step and Tracked Data
Mesh and Job
Results

## Slide 3
Units and Material
Intended Units
Units Used:
Mass: kg Length: Millimeters Stress: MPa - Newton*m-2 Force: Newtons Time: Seconds
Material - Titanium Ti-6Al-4V
Material Property:
Titanium Ti-6Al-4V (Grade 5), Annealed:
Data Used:
Density: 4.43e-6 kg*mm-3 Elastic: Youngs = 113.8e3 MPa, 0.342 Plastic: Yield = 880 MPa, Plastic Strain = 0, Ultimate = 950 MPa, Ultimate Strain = 0.14

## Slide 4
Parts and Assembly
Part Descriptions
Assembly Instructions:
Linear Pattern horizontal and vertical struts
Rotate Diagonal Strut about the vertical axis
Translate Sphere Part to one corner coincident with a horizontal strut end center
Linear Pattern Sphere Part to all corners of unit cell
Merge all Instances into one SCBCC Unit Cell Part
Linear Pattern and Merge the new SCBCC Unit Cell into a 1x2x1 Column Part
SCBCC 1 x 2 Column Assembly
Simple Cubic Body Centered Cubic, Unit Cell:
Strut Part Dimension Lengths:
Horizontal Strut Lengths: 100mm
Total Diagonal Strut Length: 173.21mm
Strut Radius: 10mm
Rounded Corner Part:
Sphere Diameter: 10mm

## Slide 5
Boundary Conditions
BCs and Reference Points
Boundary Conditions:
  Displacement applied to top center RP with B.C. for top surface
  Top Center RP at (50, 200, 50)
  Fixed Base in all translational and rotational directions
  Fixed Top in directions U1, U2
Constraints
Displacement Constraint:
  Apply displacement to Top Center RP and Rigid Body Tie Constraint to the top surface set
  Ensure the BC applied allow the top surface of the column to move rigidly with the Top Center RP compression displacement

## Slide 6
Step and Tracked Data
Time and Displacement Step
History Output:
At load RP set: RF1, RF2, RF3, U1, U2, U3
History
Step Parameters:
Loading Step: Static, general
Non-linear geometry
10,000 increments, 0.01s initial, 1e-8s smallest, 0.1s max

## Slide 7
Mesh and Job
Meshing and Seeding
Creating the Job
Create a Job for a 30mm Vertical Displacement:
Relocate as many processors that are available to run the Simulation (duration can vary depending on processor allocation)
Monitor job for distortion errors or nonlinear warnings

## Slide 8
Results
Bottom ISO View
Top ISO View
XY- Plane Perspective
Watch Videos of 30mm Displacement Results:

## Slide 9
Example Reactionary Force vs. Displacement Data:

## Slide 10
Plot Data for Reactionary Force vs. Displacement with Python:

## Slide 11
Resulting Graph
Reactionary Force vs Displacement Graph

## Slide 12
  Thank you for your time!
  Contact the following Email with any questions:
  AlecPerkins@UCSB.edu
Credits